## Slide 1
Seismic instrument problems
Jiayuan Yao, 2020/06/25

## Slide 2
Clock error
  Zhu, G., Yang, H., Lin, J., Zhou, Z., Xu, M., Sun, J., & Wan, K. (2019). Along-strike variation in slab geometry at the southern Mariana subduction zone revealed by seismicity through ocean bottom seismic experiments. Geophysical Journal International, 218(3), 2122-2135.
Seismometer misorientation
  Stachnik, J. C., Sheehan, A. F., Zietlow, D. W., Yang, Z., Collins, J., & Ferris, A. (2012). Determination of New Zealand ocean bottom seismometer orientation via Rayleigh-wave polarization. Seismological Research Letters, 83(4), 704-713.
  Wang, X., Chen, Q. F., Li, J., & Wei, S. (2016). Seismic sensor misorientation measurement using P‐wave particle motion: An application to the NECsaids Array. Seismological Research Letters, 87(4), 901-911.
  Zheng, H., Fan, J., Zhao, D., Li, C., Dong, D., Zhang, G., & Wang, X. (2020). A new method to estimate ocean-bottom-seismometer orientation using teleseismic receiver functions. Geophysical Journal International, 221(2), 893-904.
Instrument gain problem
  Park, S., & Ishii, M. (2019). Detection of instrument gain problems based on body‐wave polarization: Application to the Hi‐net array. Seismological Research Letters, 90(2A), 692-698.
Waveform clipping
  Yang, W., & Ben-Zion, Y. (2010). An algorithm for detecting clipped waveforms and suggested correction procedures. Seismological Research Letters, 81(1), 53-62.

## Slide 3
Outline
Introduction to seismograph
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping

## Slide 4
Seismograph
seismometer
data logger
https://www.iris.edu/hq/inclass/fact-sheet/how_does_a_seismometer_work
seismogram
A seismograph is a device for measuring the movement of the earth.
It consists of a ground-motion detection sensor (called a seismometer) coupled with a recording system (called data logger).
The recorded ground motion is called seismogram.
http://www.usarray.org/public/about/how#anchor1
A cartoon shows how a seismograph works

## Slide 5
EOS-Myanmar network
https://www.youtube.com/watch?v=MZ0yiINuYm4

## Slide 6
Seismograph
Sensitivity: as small as meter (i.e., 1 nm)
  The 2004 M9.1 Sumatra earthquake creates ground motions over the entire Earth that can be several centimeters ( nm)
Sources of ground motion
  earthquake, volcano eruption, explosion, ocean waves, wind, human activity (e.g., walking & driving cars), …
https://www.iris.edu/hq/retm/event/6450
20190126T03:51:37.870
Mw: 6.2
Depth: 355 km
Earthquake
EW01
Instrument response is removed
Time (second)
bp co 0.02 0.2 p 2 n 2
not filtered
Displacement (nm)

## Slide 7
Key information：
  Arrival time
  Amplitude
  Waveform
South America
Three-component seismograph (USA)
Stein & Wysession, 2003
Love
Lay & Wallace, 1995
Seismogram

## Slide 8
Some seismic instrument problems
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping
http://www.usarray.org/public/about/how#anchor1
https://www.iris.edu/hq/inclass/fact-sheet/how_does_a_seismometer_work
Lay & Wallace, 1995

## Slide 9
Outline
Introduction to seismograph
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping

## Slide 10
Clock error
http://www.usarray.org/public/about/how#anchor1
Clock error: the internal clock of the seismograph is wrong
The synchronization with Global Positioning System (GPS) is one option for on-land station.
The timing of an Ocean Bottom Seismograph (OBS) station depends on its own internal clock, which is only synchronized with GPS before deployment and after recovery.

## Slide 11
Clock error detection and correction
An OBS deployment near Mariana trench
Zhu, 2019, GJI

## Slide 12
Clock error detection and correction
Teleseismic event method
Zhu, 2019, GJI
For teleseismic events from nearby locations, differential travel time between two nearby station should stay stable.

## Slide 13
Clock error detection and correction
Zhu, 2019, GJI
The lag time of the ambient noise cross-correlation function should stay stable.
Ambient noise cross-correlation function

## Slide 14
Clock error detection and correction
Ambient noise cross-correlation function
Zhu, 2019, GJI

## Slide 15
Outline
Introduction to seismograph
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping

## Slide 16
Seismometer misorientation
ZNE components
ZRT components
II.AAK.00.BHZ.SAC
II.AAK.00.BHN.SAC
II.AAK.00.BHE.SAC
Typical sac file names
http://service.iris.edu/irisws/rotation/docs/1/help/
Azimuth and backazimuth
band code
instrument Code
orientation Code
https://ds.iris.edu/ds/nodes/dmc/data/formats/seed-channel-naming/
channel code

## Slide 17
Seismometer misorientation
The true orientations of those three components could not be consistent with what their names mean.
http://service.iris.edu/irisws/rotation/docs/1/help/
II.AAK.00.BHZ.SAC
II.AAK.00.BHN.SAC
II.AAK.00.BHE.SAC
Typical sac file names

## Slide 18
Seismometer misorientation detection methods
Zheng, 2020, GJI
If there is no misorientation, we can rotate NE to RT components correctly.
If there is a misorientation (), we will have a wrong RT components without any correction.
The rotated components are along rt directions instead of the RT directions.

## Slide 19
Seismometer misorientation detection methods
We can use the properties of seismic waves to detect the misorientation. For example,
Z
R
P-wave
Rayleigh-wave
Station
Rayleigh-wave polarization: particle motion in ZR plane
P-wave polarization: particle motion in ZR plane
http://service.iris.edu/irisws/rotation/docs/1/help/
https://www.youtube.com/watch?v=2rYjlVPU9U4
https://www.youtube.com/watch?v=6yXgfYHAS7c

## Slide 20
Seismometer misorientation detection methods
Rayleigh-wave polarization
  Stachnik, J. C., Sheehan, A. F., Zietlow, D. W., Yang, Z., Collins, J., & Ferris, A. (2012). Determination of New Zealand ocean bottom seismometer orientation via Rayleigh-wave polarization. SRL, 83(4), 704-713.
P-wave polarization
  Wang, X., Chen, Q. F., Li, J., & Wei, S. (2016). Seismic sensor misorientation measurement using P‐wave particle motion: An application to the NECsaids Array. SRL, 87(4), 901-911.
  Zheng, H., Fan, J., Zhao, D., Li, C., Dong, D., Zhang, G., & Wang, X. (2020). A new method to estimate ocean-bottom-seismometer orientation using teleseismic receiver functions. GJI, 221(2), 893-904.

## Slide 21
Seismometer misorientation detection methods
Rayleigh-wave polarization
Stachnik, 2012, SRL
Zheng, 2020, GJI

## Slide 22
Seismometer misorientation detection methods
P-wave polarization
  original P-wave waveform (Wang et al., 2016, SRL)
principal component analysis (PCA)
minimize T-component energy
Zheng, 2020, GJI
We can PCA to find directly, and then the misorientation .
We can also grid search to find one which minimizes T-component energy.

## Slide 23
Seismometer misorientation detection methods
P-wave polarization
  original P-wave waveform (Wang et al., 2016, SRL)
Wang et al., 2016, SRL
principal component analysis (PCA)
minimize T-component energy

## Slide 24
Seismometer misorientation detection methods
P-wave polarization
  P-wave receiver function (p-RF) (Zheng et al., 2020, GJI)
Zheng, 2020, GJI
Three velocity models
Amplitude of p-RF at t=0

## Slide 25
Seismometer misorientation detection methods
Zheng, 2020, GJI
Amplitude of p-RF at t=0
Y24
Y33
Y20
Y05
Y39

## Slide 26
Seismometer misorientation detection methods
Zheng, 2020, GJI
Before correction
After correction
Before correction
After correction

## Slide 27
Outline
Introduction to seismograph
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping

## Slide 28
Instrument gain problem
Park and Ishii, 2019, SRL
Where there are three threshold angles,
Four criteria used to detect gain problem

## Slide 29
Park and Ishii, 2019, SRL
Instrument gain problem

## Slide 30
Park and Ishii, 2019, SRL
Instrument gain problem

## Slide 31
Outline
Introduction to seismograph
Clock error
Seismometer misorientation
Instrument gain problem
Waveform clipping

## Slide 32
Waveform clipping
Yang and Ben-zion, 2010, SRL
Features of clipped waveforms:
Clipped waveforms contain points with amplitude close to the upper range of the recorded data.
Clipped points are in waveform portions with amplitude close to the peak value in the seismogram.
Clipped points are located within waveform sections having large amplitude fluctuations.
Clipped points have zero amplitude values.
Data on both sides of a clipped point have the same sign or one neighboring point is also zero.
upper range
clipped points

## Slide 33
Waveform clipping
Yang and Ben-zion, 2010, SRL
An automatic detection algorithm:
Treat waveforms with maximum amplitudes larger than a given threshold (e.g., 60% of the Observed Range) as potentially clipped waveforms.
For each potential clipped waveform, assume that points with zero amplitude, between the first and last samples with absolute values larger than 0.5 of the waveform peak amplitude, are tentatively clipped.
Require that clipped samples are bounded on both sides by points with the same sign or another zero.
Require that the maximum or minimum value of ± 10 samples on either side of the candidate clipped points is larger than 0.8 of the waveform peak amplitude.

## Slide 34
Conclusions
We introduce some seismological methods to detect and correct some seismic instrument problems:
  clock error
  seismometer misorientation
  instrument gain problem
  waveform clipping
We have to be very careful to do data quality analysis before using them to study the seismic source and structures.